## Slide 1: FUEL CELLS

## Slide 2: Introduction
Intention of this report:
  Provide public information about fuel cells
Discovery of the principle
1801
1839
„Gas battery“ as first fuel cell
1960s
First use in space missions
1980s
First use in in submarines
1990s
Developement of large stationary fuel cells
Commercial use as portable energy source
2007
Honda is leasing first fuel cell vehicle
2008
Commerzialisation of micro fuel cells
2009
Discuss fuel cell as an alternative
Give a short industry overview

## Slide 3: PRODUCT PERSPECTIVES
Hydrogen
Oxygen
Water
MAIN PRINCIPLE
Combine Hydrogen and Oxygen to produce electricity
PROBLEM
Where to find Hydrogen?

## Slide 4: PRODUCT PERSPECTIVES
MAIN PRINCIPLE
Combine Hydrogen and Oxygen to produce electricity
PROBLEM
Where to find Hydrogen?

## Slide 5: PRODUCT PERSPECTIVES
TYPE | TEMPERATURE (°C) | Fuel | Electrolyte
PEMFC | 40-90 | H2 (/CO2) | Polymer
AFC | 40-200 | H2 | KOH
DMFC | 60-130 | Methanol | Polymer
PAFC | 200 | H2 (/CO2) | Phosphoric Acid
MCFC | 650 | CH4, H2, CO2 | Molten Carbonate
SOFC | 600-950 | CH4, H2, CO2 | Solid Oxide
Noble metals
Non-metals/ Non-noble metals
Non-noble metals

## Slide 6: PRODUCT PERSPECTIVES
Chart: Operating temperature ranges
| PEMFC | AFC | DMFC | PAFC | MCFC | SOFC
 | 40 | 40 | 60 | 200 | 650 | 600
 | 50 | 160 | 70 | 10 | 10 | 350
Chart: Typical Output Power
| PEM WC | PEM AC | HT PEM | AFC | DMFC | PAFC | MCFC | SOFC
 | 1 | 0.001 | 0.1 | 1 | 0.001 | 25 | 50 | 0.001
 | 99 | 0.999 | 9.9 | 4 | 0.999 | 100 | 75 | 124.999

## Slide 7: PRODUCT PERSPECTIVES
TRANSPORTATION | PORTABLE | STATIONNARY
Forklift trucks and other goods handling vehicles | Military applications | Off-line short run-time systems for telecommunication base stations
Two- and three-wheeler vehicles | Auxiliary Power Units (APU) | Off-line extended run-time systems for critical communication base stations
Light duty vehicles (LDVs), such as cars and vans | Portable products | Off-line extended run-time rack mountable systems for data centres
Buses and trucks |  | On-line rack mountable systems for data centres
Trains and trams |  | Off-line systems for residential use
Ferries and smaller boats |  | 
Manned light aircraft |  | 
Unmanned vehicles |  | 

## Slide 8: REGIONAL FOCUS

## Slide 9: REGIONAL FOCUS - ASIA
Asia :
Asia is currently the leading market for fuel cells.
-Japan
Biggest Market in terms of units.
- South Korea
Biggest Market in terms of Megawatts.

## Slide 10: REGIONAL FOCUS - EUROPE
Europe :
Large and diverse fuel cell industry.
- Research Institutes are researching fuel cells
- Big markets for fuel cell buses and cars
- Germany is currently the biggest market for stationary fuel cells

## Slide 11: REGIONAL FOCUS – N.AMERICA
North America :
Fuel cell bus delivery demo program taking place in British Columbia.
Fuel cell electric vehicles are running on the streets of southern California, the government also installed a few FC stations.
FC used as backup power source for the telecom segment.

## Slide 12
REGIONAL FOCUS – REST OF WORLD
Caribbean region- off grid power FC
South African region- telecom backup & portable FC
Caribbean region- off grid power FC
Australia – minor market region

## Slide 13: DATA COLLECTION
Questions | Indicators | Data collection |  |  | 
 |  | sources | methods | sample | timing
What was the estate of the industry in 2014? (before 2015) | MW sold; Units shipped; Leading countries; Market leaders; Incentives | Older Industry analysis reports | Document review | ???? | ????
How do fuel cells work? | Number of products; | Web resources; Student’s lab | Document Review; Interview | ,???? | ?????
What are the main applications for fuell cells? | Type of services; | Web resources | Document review | ????? | ?????
What are the innovation fields? | Company names; Projects; | Web resources | Document Review | ????? | ?????
What are the alternative technologies? | Products; Concepts | Web resources | Document Review | ????? | ?????

## Slide 14: Law and governmental influence
Compare institutional environment
Starting point for research: USA, Japan, Germany (EU)
Including subsidies and other governmental support or discouragement

## Slide 15: LOGIC MODEL
Resources
4 Team members
Activities
Read IAR, extract structure
Outcomes
IAR
Lab & Supervisor
Documentation about IAR
Documentation about fuel cells
Office supplies
Outputs
Have knowledge about global fuel cell industry (e.g. technology, application, manufacturers, risks, opportunities
Build a structure for our IAR
Read about fuel cell and surrounding industry
Collect data
Collaboration with chemistry lab
Being able to identify needs of the market
Ability to write an IAR
IAR available for other people
Interact with the chemistry lab